## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26123
Problem Statement Title -
Theme - Smart Automation
PS Category - Software
Team ID -
Team Name (Registered on portal) – Hacker’s Home
Edge-AI Based Distributed Fleet Coordination for Autonomous Mobile Robots (AMRs) in Smart Warehouses

## Slide 2: HARMONI Hierarchical Adaptive Resilient Multi-robot Orchestration Network Infrastructure
Hacker’s Home
Proposed Solution
CORE UNIQUENESS — DECENTRALIZED, EDGE-FIRST COORDINATION
Every AMR carries the full coordination + autonomy stack — no central server sits in the control or safety loop, at any operating tier.
CORE COORDINATION MECHANISMS
Space-time reservations
Robots claim shared cells/aisles for specific time windows; conflicts break by a deterministic priority order.
Deadlock detection & resolution
A wait-for-graph flags cyclic waits across robots; the lowest-priority robot yields to break the cycle.
Distributed task allocation
Robots bid for tasks via a decentralized auction; tasks are leased and reassigned automatically on timeout or failure.
RESILIENCE LADDER
1 · Infrastructure mode
Wi-Fi + WMS — full fleet visibility
2 · Local P2P mode
Zenoh pub/sub over Wi-Fi Direct / local AP
3 · Isolated autonomy
LiDAR/camera only; other robots treated as obstacles
4 · Safe mode
Stop / crawl if on-board perception also degrades
5 · Recovery & resync
Resyncs state, resumes infra mode (WiFi connection restored)— loops back to stage 1

## Slide 3: TECHNICAL APPROACH
Hacker’s Home
TECHNOLOGY STACK
ROS 2
Nav2
Wi-Fi Direct / local AP (simulated)
Gazebo / Ignition simulation
CORE ALGORITHMS
Path planning: A* with event-driven replanning when costmaps change
Conflict resolution: space-time reservation table, deterministic tie-break
Deadlock handling: wait-for-graph detection, priority-based yield
Task allocation: distributed auction (CBBA-inspired), lease-based reassignment
SIMULATION & VALIDATION SETUP
Simulated world
Gazebo/Ignition warehouse map — aisles, shelves, dynamic obstacles
Simulated agents
N AMR instances, each running the full ROS 2 stack
Network emulation
Software fault injection triggers P2P / isolated-mode transitions
Metrics logging
SOFTWARE ARCHITECTURE
Edge AI
ETA/congestion prediction feeds route cost.
Fleet coordination
Intent, reservations, deadlock detect, auction
Local autonomy (Nav2)
Global/local planning + costmaps
Perception & safety
Sensor-processing pipeline, collision monitor — overrides above
Simulated robot interface
Gazebo/Ignition plugins emulating motors, sensors, network
HARMONI COMPONENT
Decentralized comms → Zenoh P2P pub/sub
Intent sharing → periodic intent broadcast
Collision avoidance → Nav2 + sensor-based safety layer
Deadlock resolution → wait-for-graph + priority yield
Dynamic rerouting → event-driven costmap replanning
Distributed task allocation → decentralized auction
Edge-only operation → per-agent compute model, no cloud/server
Eclipse Zenoh (P2P middleware)

## Slide 4: FEASIBILITY AND VIABILITY
Hacker’s Home
WHY THIS IS BUILDABLE
ROS 2, Nav2, and Eclipse Zenoh are mature, actively-maintained open-source components.
A software-only deliverable — fully buildable and testable in simulation, no physical hardware required.
SIMULATION DEMO SCENARIO
3+ simulated AMRs in a Gazebo/Ignition warehouse world; baseline run under infra Wi-Fi coordination
Induced Wi-Fi drop → observe local P2P takeover
Two robots routed into conflict → observe deadlock detection + resolution
Aisle blocked mid-route → observe dynamic reroute
Simulated robot fault → observe task reassignment
Infra restored → observe reconnect and state resync
Metric | Target
Task completion time vs. stop-and-wait | ≥20% reduction (target)
Collisions across all trial runs | 0 (validation target)
Deadlock resolution latency | To be measured in trials
Reroute trigger after aisle block detected | To be measured in trials
Task reassignment after simulated fault | To be measured in trials
Risk | Mitigation strategy
Simulated network-fault timing may not exactly match real Wi-Fi Direct/mesh radios | Model transitions on published Wi-Fi Direct latency figures; treat as a software assumption, refined once hardware deployment is scoped
Edge AI competing with Nav2 + perception for a constrained compute budget | Keep prediction models lightweight, run at low frequency, strictly outside the control loop
Symmetric conflicts causing livelock at intersections | Deterministic tie-break rule (robot ID + timestamp) guarantees a total order
MEASURABLE KPIS (PROPOSED TARGETS)
KEY RISKS AND MITIGATION

## Slide 5: IMPACT AND BENEFITS
Hacker’s Home
WHO BENEFITS
Economic
Higher AMR throughput and lower idle/stop-and-wait time directly reduce per-unit warehouse operating cost.
Operational resilience
Fleet keeps functioning during Wi-Fi/server outages — relevant to BEL's defense and strategic-logistics warehousing where infrastructure may be contested or unreliable.
Scalability
A software-only coordination layer — no added infrastructure or hardware dependency to scale to larger fleets.
Environmental
Optimized routing and reduced idle dwell time lower energy consumption per completed task.
TARGET PERFORMANCE VS. BASELINE
PROPOSED TARGET
Chart: Relative completion time
| Stop-and-wait coordination | HARMONI (P2P coordinated)
Avg. task completion time (relative units) | 100 | 78
Proposed target: ≥20% reduction in average task completion time vs. stop-and-wait, at a zero-collision validation target — not yet measured; to be validated entirely through Gazebo/Ignition simulation trials.

## Slide 6: RESEARCH AND REFERENCES
Hacker’s Home
Reference and Research work
Gazebo : https://gazebosim.org/docs/latest/getstarted/
ROS 2 : https://docs.ros.org/en/jazzy/ , https://github.com/ros2/
NAV 2 : https://docs.nav2.org/rolling/ , http://github.com/ros-navigation/navigation2/
Zenoh : https://zenoh.io/ , https://github.com/eclipse-zenoh/zenoh/
Algorithms : https://networkx.org/documentation/stable/reference/index.html , https://github.com/AtsushiSakai/PythonRobotics/
Edge AI : https://onnxruntime.ai/docs/ , https://github.com/microsoft/onnxruntime/